How to install One touch Up& Down Power Window Controls in an FC RX-7

As an option to adding relays to get rid of the PW switches trouble I was having, I decided to add an  Autoloc one touch (WC2000) system to my 87 TurboII. Both the relay & Autoloc alternatives get rid of the poor design of having the motor current going through the PW switches so this will make the switches last longer. The only difference in operation is the “Power off” switch in the driver side main switch must be ON to operate the Pass. window from both the drivers side & pass. side switch.

There is a hole in the middle of the inside door frame about 6 inches in diameter. There are 2-  8mm nuts welded to the backside right next to the hole. I took a piece of sheet metal & made a `half moon`` to fill the top part of the hole & used 2 bolts to secure it using the welded nuts. That is  where i mounted the WC1000. You have to mount it on the inside of the sheet metal to clear the door upholstery. I've included pics showing this. I also have remote door locks mounted on this same piece of metal.

Access to a factory service manual will really help. Use wiring diag 50-K. I used the standard colour code for wires but in case you're not familiar with it:

B=black	R=red	L=blue 	Br= brown	W=white	G=green

BR=black with a red stripe		BL=black with a blue stripe

GB=green with a black stripe		RB= red with a black stripe

K-04 is the connector between  the main (drivers side) switch & the harness. K-06 is the T conn. between the the main PW switch & the drivers side motor. K-05 is the connector between the Pass. Side switch & the harness. K-07 is the T conn. The K-05 conn & the Pass. Side motor

One touch PW wiring changes Drivers side

- Bridge the R lead from the WC1000 to the BR lead at the harness side of the K-04 conn.

- Bridge the B lead from the WC1000 to the B lead at the harness side of the K-04 conn.

- Cut the RB lead between the K-04 conn & the K-06 conn

- wire the switch side of the RB lead to the Br lead of the WC1000

- wire the motor side of the RB lead to the G lead of the WC1000

- Cut the GB lead between the K-04 conn & the K-06 conn

    - wire the switch side of the GB lead to the W lead of the WC1000

    - wire the motor side to the L lead of the WC1000

One touch PW wiring changes passenger side

- Bridge the R lead from the WC1000 to the BL lead at the harness side of the K-05 conn

- Wire the  B lead (ground) to any bolt in the door using a ring conn.

- Cut the R lead  between the K-05 conn. & the K-07 conn.

    - wire the switch side of the R lead to the Br lead of the WC1000

    - wire the motor side of the R lead to the G lead of the WC1000

- Cut the G lead from the K-05 conn. To the K-07 conn.

- wire the switch side of the G lead to the W lead of the WC1000

- wire the motor side of the G lead to the L lead of the WC1000