SECTION 1- PRODUCT AND MANUFACTURER INFORMATION

MSDS DATE: 02/11/2003

PRODUCT                      NPG+

SYNONYMS                   Coolant

CHEMICAL FAMILY    Glycols

FORMULA                      Blend

MANUFACTURER                              EMERGENCY INFORMATION

Evans Cooling Systems, Inc

255 Route 41 North                               EMERGENCY PHONE   888-990-2665  (24-hour)

Sharon, CT 06069

860-364-5130

SECTION 2 - HAZARDOUS INGREDIENTS

CHEMICAL/COMMON NAME          CAS-NUMBER       %         PEL-OSHA                  ACGIH - STEL

ETHYLENE GLYCOL			107-21-1	≥ 69%		none established               50 ppm (ceiling)

Product is not considered carcinogenic by NTP, IARC or OSHA

SECTION 3 - HAZARDOUS MATERIAL IDENTIFICATION SYSTEM

HEALTH=2      FLAMMABILITY=0      REACTIVITY=0     	PROTECTION=B

SECTION 4 - HEALTH HAZARD DATA

HEALTH EFFECTS (Acute And Chronic)

EYES	May cause slight transient eye irritation; corneal injury is unlikely.

SKIN	Generally non-irritating.  Prolonged or repeated contact may cause flaking, tenderness and softening of the skin.

INHALATION	No adverse effects under normal usage.  However, if significant vapors or mists are inhaled, exposure may result in irritation to the upper respiratory system.

INGESTION	 Ethylene Glycol is considered toxic and may cause central nervous system depression, dizziness, headache and nausea.  Significant ingestion may lead to loss of consciousness.  Has been known to cause kidney toxicity.

PRIMARY ROUTES OF ENTRY

EYES/SKIN: Yes                     INHALATION: No              	INGESTION: Not Likely

MEDICAL CONDITIONS AGGRAVATED BY EXPOSURE  pre-existing eye disease

SECTION 5 - FIRST AID INSTRUCTIONS

EYES	Flood with water for at least 15 minutes. If irritation persists, get medical attention.

SKIN	Wash with water and mild soap.  If irritation occurs and persists, get medical attention.

INHALATION	Inhalation exposure should require no action.  However, if significant inhalation exposure has occurred, move victim to fresh air. If breathing is difficult, give oxygen. If breathing has stopped, administer artificial respiration (mouth to mouth is preferred) if trained - get immediate medical attention.

INGESTION	If victim is alert, give the victim 4 – 8 oz of water.  Do not induce vomiting.  Keep victim calm warm and seek medical advice

NOTE:  Liver damage may be indicated by loss of appetite, jaundice, fatigue and sometimes pain/swelling on

right upper abdomen.  Kidney toxicity is indicated by blood in urine or increased/decreased urine flow.  Other

signs and symptoms of exposure can include nausea, abdominal cramps and diarrhea.

SECTION 6 - CHEMICAL DATA

BOILING POINT                       375°F	                     SPECIFIC GRAVITY (WATER=1)         1.09

VAPOR PRESSURE (kPa)        8.0@176°F                       SPECIFIC HEAT @212°F                         0.66BTU/lb

VAPOR DENSITY (AIR=1)      >1.0                                  AUTOIGNITION TEMPERATURE         1054.7°f

SOLUBILITY IN WATER   complete

APPEARANCE AND ODOR INFORMATION Brown liquid, faint sweet trace odor

INCOMPATIBILITY (Materials To Avoid)  oxidizers

HAZARDOUS DECOMPOSITION PRODUCTS  none

WILL HAZARDOUS POLYMERIZATION OCCUR no

CONDITIONS TO AVOID FOR POLYMERIZATION none

IS THE PRODUCT STABLE  yes

CONDITIONS TO AVOID FOR STABILITY none

SECTION 7 – FIRE FIGHTING INFORMATION

FLASH POINT (Method Used)  233.4°F	              FLAMMABLE LIMITS  lower = 2.6%  upper = 12.6%

EXTINGUISHING MEDIA  water fog, foam, dry chemical

SPECIAL FIRE FIGHTING PROCEDURES Keep fire-exposed containers cool with water fog.  Wear SCBA and full turnout gear as recommended by NFPA.

UNUSUAL FIRE AND EXPLOSION HAZARDS  None expected under normal storage and handling conditions.  Avoid exposing product to ignition sources (sparks) or temperatures above flash or autoignition point.

SECTION 8 - SPILL OR LEAK/DISPOSAL PROCEDURES

STEPS TO BE TAKEN IN CASE MATERIAL IS RELEASED OR SPILLED

Dike and contain the spill.  Spread granular absorbent  Sweep up and place in container for disposal.  Do not allow material to enter drains, sewers and waterways.  Comply with spill all local notification requirements.  All response activities must comply with HAZWOPER (29CFR 1910.120).

WASTE DISPOSAL METHODS  Dispose of waste in compliance with local, state and federal regulations.  Recycle all wastes whenever feasible.

SECTION 9 – TOXICOLOGY INFORMATION

For ETHYLENE GLYCOL: Repeated oral exposure in experimental animals and in humans has caused kidney toxicity secondary to metabolic acidosis.  Humans are more sensitive to ethylene glycol than experimental animals.  Toxic doses are estimated to be 3 – 4 oz (approx. one-half cup) for an average human adult.

SECTION 10 – ECOLOGICAL INFORMATION

Data being evaluated.

SECTION 11 - EXPOSURE CONTROL AND PROTECTION

VENTILATION Use forced-air ventilation when handling product in a confined area

RESPIRATORY PROTECTION Not normally needed during intended usage and handling.  However, if exposure causes irritation during routine or non-routine application of product, use NIOSH/MSHA approved respiratory protection (refer to 29CFR 1910.134).

PROTECTIVE GLOVES Rubber or PVC (refer to 29CFR 1910.132)

OTHER PROTECTIVE EQUIPMENT Wear eye protection and full cover shirt and pants to protect against exposure. Provide local emergency showers and eyewash stations in the workplace

OTHER ENGINEERING CONTROLS  Use local exhaust to minimize mist or vapor levels in the work area.

WORK PRACTICES  All users should consult MSDS before handling this material.

HYGIENIC PRACTICES  Wash hands and face after using this product. Remove contaminated clothing   Launder contaminated clothing before re-use.

SECTION 12 – HANDLING AND STORAGE

PRECAUTIONS TO BE TAKEN IN HANDLING AND STORAGE   Store in a cool, dry place.  Keep all containers closed when not in use.

SECTION 13 - SPECIAL PRECAUTIONS

MAINTENANCE PRECAUTIONS    None

SECTION 14 – OTHER INFORMATION

NOTE:  This MSDS is intended to protect personnel during packaging, storage and transport of the product in bulk quantities.  It is recognized that the end-user will most likely handle (and subsequently be exposed to) less than 10 gallons of the product.

SECTION 15 – REGULATORY INFORMATION

COMPONENT INFORMATION: ( U.S.A. and Foreign  Patents Pending )

00107-21-1	Ethylene Glycol (66 – 70%) **

00057-55-6	Propylene Glycol

    - Water

- - - - - -                Proprietary Corrosion Inhibitor Package <2%

SARA INFORMATION  **Ethylene Glycol is regulated under SARA III Section 313 Supplier Notification  Requirements.

TSCA INFORMATION All components of this product are listed in the TSCA Inventory.

DOT INFORMATION

Not Regulated

SECTION 16 – HAZARDOUS MATERIAL IDENTIFICATION GUIDE

The follow letter codes refer to personal protective equipment (PPE) recommendations as shown in SECTION 3 of this MSDS, relative to handling hazardous chemical products.

A	Safety Glasses

### B	Safety Glasses, Hand Protection

C	Safety Glasses, Hand Protection, Protective Apron

D	Full Face Shield, Hand Protection, Protective Apron

E	Safety Glasses, Hand Protection, Dust Respirator

F	Safety Glasses, Hand Protection, Dust Respirator, Protective Apron

# G	Safety Glasses, Hand Protection, Vapor Respirator

H	Splash Goggles, Hand Protection, Protective Apron, Vapor Respirator

# I	Safety Glasses, Hand Protection, Dust & Vapor Respirator

J	Safety Glasses, Hand Protection, Protective Apron, Dust & Vapor Respirator

K	Air Line Hood or Mask, Hand Protection, Full Body Suit, protective Boots

X	Unspecified – to be determined*

(*special equipment selection for site-specific applications not otherwise shown here)