DIY  Electronic Compression Tester

The following compression tester was built for about $200.

There are 4 major parts for this tester

(1) Dataq DL-194RS Driver Box/Software - $24.95

http://www.dataq.com/products/startkit/di194rs.htm

(2) Measurement Specialties, Inc. Pressure Transducer - $124

MSP-300-250-P-4-N-1, 0-250 psi, 0-5 volts

http://www.mouser.com/msi/

(3) Quick Disconnect Plug Adapter

Two of the connectors are from any store selling air hose connectors,

cost about $5. The 14mm plug adapter is from a cheap mechanical tester

which cost about $30.

(4) Battery Pack (optional) - about $3 without 8 batteries.

From an electronics store. The pressure transducer needs between

10 - 30 vdc to run. My small car battery voltage drops to about 9vdc when

cranking. Thus I made this small 12vdc battery pack to insure a stable power

supply.

Minor Parts

(1) Serial to serial port connector

(2) Battery to DATAQ connector

(3) Wire to lengthen transducer cable

(4) Tie Wraps to secure wiring.