Third Generation RX-7 Widefoot Heel and Toe Adapter

Take the pedal adapter apart, but remember which  way the "U" shaped clip

goes onto pedal adapter. Take the  adapter and place it to the left of the gas pedal, matching  the right-side contour of the adapter to the left side of  the gas pedal.

Thread the enclosed 8-32 x .75 set screw into the top tapped hole (3-4 turns) of the clip.  Make sure you do not "cross thread" the set screw into the clip, it should go in easily.  Take the clip and position it behind the gas pedal, at a height such that the tapped holes line up with the  through holes in the adapter. The "open end" of the clip  should be aligned with the molded plastic shank of the gas  pedal.

Now slide the open end of the clip towards the back of the car, over the gas pedal shank. It's a tight fit  (on purpose, it increased the stability of the adapter),  but it will go on. Make sure you properly support the gas  pedal while sliding the clip, as the plastic pedal is not  nearly as strong as the aluminum of the brake or clutch.  With the clip securely seated, slip the small spacer over the set screw, in the same orientation as originally shipped.

Once the clip is pushed on, place the curved Pedal Adapter on in the same manner as when received.  Take two of the three 8-32 x 7/16" flathead screws, and very carefully start them into the two free holes.  They will go in at the same angle as the set screw.  Leave the screws slightly loose.

Remove the set screw, but don't discard it if you think you may take the WPA off at a later date (you'll need it for the re-install).  Take the remaining flathead screw and run it in loosely.

Tighten the center screw, then the lower screw, and finally the upper one.  At this point the WPA should be perfectly flush with the OEM pedal face.  If it's not, loosen the upper and lower screws, and tighten one or the other to "tip" the WPA into the right orientation.  At this point, balance tighten the two screws.

A tip - use a short #2 Phillips screwdriver that has a blade in good condition.  Use a light grade of Locktite to help fix the screws in place.

Please call me if you have any questions.  You can reach me on

my cellphone, 781-254-6022, or my work number, 603-464-2107.

Thanks for your purchase of a Widefoot Product!!

David Breslau

64 Hodge Rd.

Arlington, MA 02474