NGK PLUGS:

R7420-9 through R7420-10, Mazda racing, fine wire iridium center and platinum ground

electrode, 14mm, 21 mm reach, recessed tip, resistor, .028" gap, the best

for high power. BEST #1. expensive.

R7438-8, Nissan 370 racing, fine wire iridium center and platinum ground

electrode, 14mm, 26.5 mm reach, recessed tip, resistor, .028" gap, the best

for high power. Used with a special spacer and 2nd seal.

The above two work with a normal plug sockets.

BnEGV      fine wire gold palladium @ .025" gap, best for the price. Non resistor.

HKS now recommends resistor plugs for the TwinPower.

BRnEIX     Iridium resistor @ .032" gap.

R7376-n    racing version of above 2 plugs, 14mm, 19mm reach, fine wire iridium center

electrode, fine wire nickel ground, can be had in an 8 heat range!

BRnECMIX   Iridium resistor @ .032" gap, use only in NA engines.

The above 4 non rotary plugs require a special thin socket; Racing Beat sells it

for about $83 or cut down a good grade socket. 14mm, 3/4" reach, 13/16" hex.

AR3932X Autolite Racing Only 14mm, 19mm reach, 5/8 hex

DENSO PLUGS

IRE01-27, 31-35, Mazda plugs, iridium center, platinum ground, resitor, same sizes as NGK R6725-n plugs, .028" gap. $35, see heat range conversion chart below.

One place to order from: http://www.sparkplugs.com/

Spark plugs with "retracted and surface gap" style as compared to "extended tip" styles, require more ignition lead / advance to make best power.

| Thread size (Hexagon size) | Spark plug type | Part number | Heat range | Terminal shape | Appearance Firing end | Electrode material |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Center electrode | Ground electrode |
| φ14 x 19mm( 20.8Hex) | B-E | R6918B- | 7,8,9 | Solid post terminal |  | Platinum | Nickel |
|  |  | R7376- | 7,8,9,10 | Solid post terminal |  | Iridium | Platinum |
|  |  | R6712- | 9,10 | Thread terminal with nut |  | Nickel | --- |
| φ14 x 22mm (16.0Hex) | Short | R7282A- *2 | 10,105,11 | Solid post terminal |  | Iridium | Platinum |
| φ14 x 19mm (16.0Hex) | Short | R7282- *2 | 9,10,105,11 | Solid post terminal |  | Iridium | Platinum |
|  | BK-E (IS0/JIS) *1 | R7433- | 8,9,10 | Solid post terminal |  | Iridium | Nickel |
|  |  | R7434- | 8,9,10 | Solid post terminal |  | Iridium | Platinum |
|  |  | R6601- | 8,9,10,11 | Solid post terminal |  | Nickel | --- |
|  | BC-E (old JIS)*1 | R7435- | 8,9,10 | Solid post terminal |  | Iridium | Nickel |
|  |  | R7436- | 8,9,10 | Solid post terminal |  | Iridium | Platinum |
|  |  | R6690- | 9,10,11 | Solid post terminal |  | Nickel | --- |
| φ14 x 26.5mm (16.0Hex) | LFR(long reach) | R7437- | 8,9,10 | Solid post terminal |  | Iridium | Nickel |
|  |  | R7438- | 8,9,10 | Solid post terminal |  | Iridium | Platinum |
| φ14 x 21.5mm (20.8Hex) | Rotary Engine RX-7 | R6725- | 9,10,105,11,115 | Solid post terminal |  | Platinum | Platinum |
|  |  | R7420- | 9,10,105,11 | Solid post terminal |  | Iridium | Platinum |
| φ14 x 21mm (20.8Hex) | Rotary Engine RX-8 L | R7440A-L | 9,10 | Solid post terminal |  | Iridium | Platinum |
| φ14 x 19mm (20.8Hex) | Rotary Engine RX-8 T | R7440B-T | 10,11 | Solid post terminal |  | Iridium | Platinum |
| *1) | The length from gasket to terminal of ISO/JIS type spark plugs is 50.5mm which is 2.5mm shorter than old JIS type spark plugs. |
| *2) | It's necessary to use special plug caps |
| *3) | Resistor spark plugs are recommended for cars originally equipped with resistor spark plugs. When nonresistor spark plugs are installed in such cars, there is some possibility that the electric devices in the car, such as the audio system or the engine managemant system, would be affected by noise. |
| *4) | Heat rating number enters |

http://www.ngk-sparkplugs.jp/english/raceinfo/sparkplug/02/index.html